## Slide 1: SMS 9-1-1 New Jersey NENA Fall Meeting
November 22, 2013

## Slide 2: SMS 9-1-1 Attempts for One Carrier
> 71,000 Public SMS 9-1-1 Attempts 1/1/13 – 9/30/13

## Slide 3: SMS 9-1-1 Progress To Date
52 PSAPs in 16 states
36 use TCS GEM9-1-1 Web Portal
6 use TTY
10 Steering to Intrado
28 Public Announcements
More Announcements Soon
20 PSAPs in Process of Being Deployed
More Than 150 PSAPs in Queue
T-Mobile FOA Later This Month!
Notes: Flexible and Robust Solution
  Multiple Delivery Options to the Public Safety Answering Point (PSAP)
Real-Life Deployment Experience
  PSAP On-Boarding
  Carrier On-Boarding
Willing and Able to Support California’s Pilot and Production Needs
Recommend Three Pilots
  Two Varieties of TTY
  Web Services Interface (GEM911™)

## Slide 4: Deployment Options
GEM 9-1-1™ Web Interface
TTY
Direct IP – i3 Interface (MSRP)

## Slide 5: Anything Unexpected?
PSAPs need to have 24X7 control of their Internet access.
Web interface training is easier and faster than expected.
Location will vary among carriers.

## Slide 6: How’s it going?
  Like wireless 9-1-1, SMS 9-1-1 is being deployed in a variety of ways:
    State level, County level, PSAP level
  States are beginning to see the need to avoid fragmentation
    California
    Florida
    New Jersey
    Maryland
  Will texts from all carriers look the same?

## Slide 7: The Argument for Statewide Deployment

## Slide 8: The Argument for Statewide Deployment
Verizon Wireless Only
All Wireless Carriers
A Subset of All Carriers

## Slide 9: A Controlled SMS 9-1-1 Deployment
All Wireless Carriers

## Slide 10: Benefits
Uniformity
  Wireless Carrier Coverage
  Interfaces Between PSAPs and Carriers
  User Experience at the PSAP
Aggregation
  Reporting at the State and PSAP Levels
  Single Interface to PSAP
  “One-Throat-Choke” – No Need for the PSAP to Decipher Message in Order to Troubleshoot…..Just Call TCS
Consistent and Ubiquitous Service to the Residents of Maryland

## Slide 11: TCS GEM911 User Interface
Transfer
PSAP: XYZ County
HUNC is Graphically Represented by the Size of the Circle
New Incoming Messages
Active Sessions
Other Call Takers’ Sessions
The MDN and the Call Taker’s Username Are Shown in Each Message Next to the Timestamp
LAT/LON and HUNC Values
Drop-down With Canned Responses, or Free Type
Rebid Functionality

## Slide 12: Smart911: Integrated Subscriber Info
Smart911 Fully Integrated into GEM911 Portal
Also Offer Standard Smart911
Delivery of Rich Media to PSAP
  Medical Conditions
  Allergies
  Disabilities
  Number of Residents in Home
  Bedroom Layouts in Home
  Photos of Dependents, Pets, Residence

## Slide 13: GEM911 versus TTY
GEM911
Full Character Set
Bi-Directional Session Management (Full-Duplex)
Location Delivered with Session
Multi-Session Management
Short Deployment Timeline
Additional Data Integration
CPE Integration
IP Network Accessibility Considerations
Screen Real Estate Impact
Seamless Migration to NG9-1-1
TTY
Reduced Character Set
Uni-Directional Session Management (Half-Duplex)
Existing Automatic Location Identifier (ALI) Process for Location
Single-Session Management
Longer Deployment Timeline
Possible Cost Impacts
CPE Integration - Logging and Reporting
Reuses Existing Overload Trunking Policy
Operational Familiarity

## Slide 14: SMS 9-1-1 PSAP Deployment Process
Pre-Deployment
  PSAPs/State Request SMS 9-1-1 Service From Wireless Carriers
  PSAPs Fill Out Checklist to Ensure Technical Readiness
Deployment
  Hold Kick-Off and Project Status Calls
  Provision PSAP Details
  Provision PSAP Boundaries
  Conduct PSAP Training
  Perform Testing and Turn-up
Support
  24x7 Maintenance and Troubleshooting
  TL 9000-Certified Network Operations Center

## Slide 15: Current TCC Deployment Architecture
PSAPs
Carriers
Text
Control
Center
Legacy PSAP (TTY)
Transitional PSAP (GEM)
Next Generation
PSAP (i3 MSRP)
Notes: Robin
Deployments of SMS to 9-1-1 by the carrier are not linked to PSAP deployment timelines
Carriers deploy market by market, & national rollout
PSAP deployment by State / County / Jurisdiction / PSAP based individual plans by request
Matched geographic deployment requires a high level of coordination with timing & resource issues.
ATIS J-STD-110 promotes a standards based architecture
TCC deployed by the carrier toward the PSAP must support
  3 types of downstream messaging
    TTY
    Web Services (HTTPS Client/Server)
    i3 ESInet
  Individual links (x2 if redundant) = to number of PSAPs

## Slide 16: Multiple Service Provider Challenge
PSAPs
Carriers
TCC 1
TCC 2
TCC 3
TCC 4
Legacy PSAP
Transitional PSAP
Next Generation
PSAP
Notes: Robin
ATIS J-STD-110 Supports Origination Provider TCC
  Requirement for each carrier to operate or integrate with a TCC
  Examples show single TCC architecture
  Network design challenges with a single TCC
    Carrier operated TCC leads to a large number of direct PSAP links
    Jurisdiction operated TCC doesn’t work
      Repeated Deployments – Continuous carrier integration required as PSAPs all over the US request SMS to 9-1-1 service
      Requires re-integration at each PSAP for each new carrier that brings up SMS to 9-1-1 service
    Numbers of circuit connections to all 6000+ PSAPs becomes immensely staggering - an exercise in circuit multiplication

## Slide 17: EMedia Architecture – Interconnectivity Solution
PSAPs
Carriers
State
SIP
HTTPS
SIP
TCC
TCC 2
TCC 3
EMedia
GW
Legacy PSAP
Transitional PSAP
Next Generation
PSAP
TTY
Notes: TCS proposes “symmetric” TCC architecture
  TCS introduces EMInet, a combination messaging architecture that merges specifically defined TCC functions
    EMedia Aggregation Gateway
    EMedia Distribution Server
  Carrier TCC and PSAP TCC work together for efficiency
    EMedia Aggregation Gateway is a carrier operated TCC that handles incoming SMS messages
    EMedia Distribution Server is a PSAP operated TCC that delivers text messages over the appropriate protocol to the PSAP
    EMedia elements inter-communicate using standard SIP/MSRP
  Reduces deployment hassles
    Carrier deployment of EMedia Aggregation Gateway integrates directly with one or more regionally deployed EMedia Distribution Server(s)
    Reduces interconnection (circuit) costs

## Slide 20: Questions?

## Slide 21: Thank you!

## Slide 22: Acronyms
Acronym | Definition
ALI | Automatic Location Identifier
CPE | Customer Premise Equipment
DB | Database
ECaTS | Emergency Call Tracking System
EMInet | Emergency Media Internet Protocol Network
ESInet | Emergency Services Internet Protocol Network
ESRK | Emergency Services Routing Key
FCC | Federal Communications Commission
HTTPS | Secure Hypertext Transfer Protocol
HUNC | Horizontal Uncertainty
IP | Internet Protocol
LAT/LON | Latitude, Longitude
LSRG | Legacy Selective Router Gateway
MDN | Mobile Directory Number
MF | Multi-Frequency
MIS | Management Information System
Acronym | Definition
MSC | Mobile Switching Center
MSRP | Message Session Relay Protocol
NENA | National Emergency Number Association
NG9-1-1 | Next Generation 9-1-1
POI | Point-of-Interconnection
PSAP | Public Safety Answering Point
SIP | Session Initiation Protocol
SMS | Short Message Service
SR | Selective Router
SSP | System Service Provider
TCC | Text Control Center
TCS | TeleCommunication Systems, Inc.
TDM | Time Division Multiplexing
ToIP | Text over Internet Protocol
TTY | Teletype
WSP | Wireless Service Provider